## Slide 1: sdmay19-17: Burns and McDonnell Substation Design
Tom Kelly, Connor Mislivec, Jake Heiller, Rebecca Franzen,
Wilson Pietruszewski, Riley O’Donnell

## Slide 2: Client Overview
Engineer-architect-contractor consulting firm
Headquartered in Kansas City, Missouri
Notes: Been working with Grant Hermann
Bi-weekly meetings on the phone
Next semester will be working with Thanh Nguyen and Zach Porter
Burns and McDonnell: client and advisor
Consulting firm: many specs given to us by client
What is consulting?
Providing design phase services for cyclone substation -- interconnection for a new wind farm being built in the area
Physical construction is contracted out.

## Slide 3: Problem Statement
General problem
  High voltage distribution is unsafe
  Unable to transmit power long distances
Our solution
  Design 138/69 kV greenfield substation
  Regulate voltage levels in/out
  Ring bus configuration
http://gannettfleming.com/Projects/2015/10/19/11/29/mill-electrical-substation-upgrade

## Slide 4: Conceptual Sketch
138/69 kV XFMR
69 kV Breaker
138 kV Breakers
Line to Des Moines
Line to Cedar Falls
Notes: Talk about how we preliminarily came up with the layout for the substation and how we proceeded to design the substation afterwards

## Slide 5: System Block Diagram
Studies pt. 1
Physical Design
Studies pt. 2
P&C
Notes: Talk about how our project is unique and we have already completed part of the design

## Slide 6: Operating Environment
Built to last
Withstand regional weather extremes
Notes: Add image of old substation versus new substation

## Slide 7: Technical/Other Constraints/Considerations
Three 138 kV Circuit Breakers
One 69 kV Circuit Breaker
One 138/69 kV Transformer
Ring Bus Configuration
Future “Breaker-and-a-half” Scheme
Two transmission lines entering/exiting substation
Grounding System withstand 21 kA Fault Current
Site Size of 400’ x 400’
http://eblogbd.com/detils-air-insulated-substations-bus-switching-configurations/

## Slide 8: Functional Requirements
Site Design & Substation Layout
Bus & Insulator Sizing Design
Ground Grid & Lightning Protection
Raceway
Control Building
125VDC Station Battery Design
Relaying & Controls
Communications
Notes: Refer to BMcD’s Scope of Services document, Refer to IEEE documents that are or will be used 998, 485, 80

## Slide 9: Market Survey
Upward trend in energy consumption
New technology for protection
  Infrastructure attacks
  Reducing blackouts
Substations are becoming outdated
  Need for system upgrade
Notes: Graph of US electrical energy consuption
Image of old vs new substation
Federal energy regulatory commision
North American Energy Reliability Corporation

## Slide 10: Potential Risks and Mitigation
Potential Electric Shock due to Fault Current
  Grounding System designed to provide safe environment to those within the vicinity of the substation.
  Lightning Protection Design to provide protective layer over major equipment
Faulty testing software

## Slide 11: Resource Estimate

## Slide 12: Schedule: Semester 1
3 deliverables
  Grounding design- November 2
  Lightning Protection Design- November 2
  Physical Design- November 30

## Slide 13: Schedule: Semester 2
2 deliverables
  AC/DC Studies- March 1
  Controls and NIA- April 12

## Slide 14: User Interface Description
Communications systems
Service Centers
  Centers for Data Aggregation and Grid power control

## Slide 15: Functional Decomposition
Physical Design Package
  Grounding System Design
  Lightning Protection Design
  Physical Design Drawings
Preliminary Grounding Design
Physical Drawing Plans
  Plan View
  Elevation Views
Update Grounding Design based on Plan View
  Include major equipment
Lightning Protection Study
Physical Lightning Protection Plan Drawing

## Slide 16: Software Programs used
CDEGS- (Current Distribution, Electromagnetic Interference, Grounding and Soil Structure Analysis)- Grounding (earthing) and electromagnetic analysis software package; used in ground grid design process.
AutoCAD- Computer-Aided design and drafting software; used in the creation of physical drawings.

## Slide 17: Detailed Design (Grounding System Design)

## Slide 18: Testing
Notes: Talk about rocks

## Slide 19: Testing Continued

## Slide 20: Detailed Design (Lightning Protection)
Notes: Protection of an exposed object by a single lightning mast

## Slide 21: Detailed Design (Lightning Protection)
Notes: Protection of an exposed object by two lightning masts

## Slide 22: Detailed Design (Physical Design)

## Slide 23: Detailed Design (Elevation A-A)

## Slide 24: Detailed Design (Elevation B-B)

## Slide 25: Project Status
Submitted deliverables to client on November 30
  Physical Design Package
  Grounding Design Package
  Lightning Protection Design Package

## Slide 26: Plan for next semester
AC/DC Studies
  Battery Sizing
Relaying and Controls
  Protection schematics and wiring diagrams
Communications
  Fiber communications between substations